## Slide 1: From disk drives to cloud storage
Dr. Ping Huang
Principal Engineering at OCI

## Slide 2: Agenda
Behind the Cloud Storage
  Disk Technology Basics
  NPI Disks to the Cloud
  Sustaining Disk Based Storage Systems
  EOL Disk Drives
Cloud Storage
  Concept and definition
  Cloud Storage Architecture
  Storage Virtualization

## Slide 3: Disk Technology Basics
What is common among the EC2, EFS, EBS, S3?

## Slide 4: Disk Technology Basics
What is common among the EC2, EFS, EBS, S3?
Storage Media
Storage Media be categorized based on
  Media Technology: Hard Disk Drive (HDD) and Solid State Drive (SSD)
  Interface to Host: SATA , SAS, NVMe

## Slide 5: HDD Characteristics
Based on Magnetic Theory
Multiple Disk Heads corresponding to disk platters
Mechanical Actuators to drive Disk Heads
Servo System to help position heads, i.e., called seeking
Disk platters are spinning while the disk is seeking
Data is organized as Sectors on the disk tracks
Shingle Magnetic Recording (SMR) HDD improves capacity
Poor random performance, but good sequential performance
Cheap $/GB, 25T/26T per drive

## Slide 6: SSD Characteristics
Mainly Based on NAND Flash Memory, SLC, MLC, TLC, QLC
Read, Write/Program, Erase operations, in page and block units
Overprovisioning Space to make an SSD workable
Flash Translation Layer (FTL) to mask these idiosyncrasies
Garbage Collection (GC) to reclaim space
High performance and lower power consumption
Limited lifespan in P/E cycles

## Slide 7: NPI disks to The Cloud
Hyper-scale customers have different requirements than other market segments
  Unique operating environments, i.e., managed data centers
  Large volume of buy-in, allowing customization
  Performance, reliability, energy-efficiency
  Typically, long-term partnership
Customers:
  AWS, Azure, GCP, Meta Platform, Apple, Tiktok
SSD OEMs:
  Samsung, Sk Hynix, Intel(Solidigm), Micron, Western Digital, Toshiba
Server ODMs Providing EMS:
  Foxconn, Quanta

## Slide 8: Roles of the parties during NPI
Customers
  Plan on the projects
  Define project requirements: performance, durability, thermal spec, etc.
  Communicate requirements to OEMs
  Instruct ODMs on building and testing servers
  Coordinate collaboration between OEMs and ODMs
SSD OEMs
  Propose new SSD products/features to customers
  Align with customers on technical roadmap, e.g., quarterly
  Address customer requirements
  Conduct adequate in-house testing

## Slide 9: Roles of the parties during NPI
Server ODM:
  Plan on resources for customers’ projects
  Perform the tests per customers’ request
  Provide test reporting to customers
  Monitor progress is on schedule
  Track issues encountered during the testing
  Work with both OEM and Customer to address issues
Customer
ODM
OEM

## Slide 10: Roles of the parties during NPI
Server ODM:
  Plan on resources for customers’ projects
  Perform the tests per customers’ request
  Provide test reporting to customers
  Monitor progress is on schedule
  Track issues encountered during the testing
  Work with both OEM and Customer to address issues
Customer
ODM
OEM
Disk drives are qualified for the specific project !! Congrats!

## Slide 11: In the field
Drives are constantly failing or malfunctioning
  Drives become slow
  Data inconsistency
  Drive dropping
  Drive hung
Various reasons
  Software bugs
  Human incidents, e.g., misconfiguration
  Firmware bugs
  Hardware breakdown
  Thermal violation

## Slide 12: monitoring
S.M.A.R.T Technology
  Self-Monitoring, Analysis, Reporting, Technology Attributes
  These attributes are indicative of the drive’s health
  Each server runs an agent which periodically collects and sends SMART a database
Dashboard
  Host of SMART attributes
  Visualization for easy check of trends
  Data Analysis and Machine Learning to gain insights from the data
Fleet Management
  Instance migration
  Storage migration
  Server isolation
  Firmware update

## Slide 13
.
.
.
SMART
SMART
SMART
Servers
Dashboard
Migration/ Isolation
Fleet Management

## Slide 14: EOL Disk Drives
When the server reaches end of service life
  Retire the server and disk components
  Ensure data is not subject to leakage
Data Eradication Process
  Software approach
  Disk cleaning via security erase and data sanitization
Media Destruction Process
  Physical approach
  Destroy the drives

## Slide 15: Cloud Storage
What is Cloud Storage ?
  Cloud Storage refers to the practice of storing digital data on remote servers, typically managed by third-party providers, rather than on locally. It allows individuals and organizations to save their files on servers maintained by cloud service providers and access their data from any internet-connected device, at any time, and from virtually anywhere in the world.
  Cloud Storage can be characterized by: Remote Data Storage, Accessibility, Scalability, Security, Cost-effectiveness
  Types of Cloud Storage: Personal Cloud Storage, Enterprise Cloud Storage, Hybrid Cloud Storage
  Cloud Storage Providers: Amazon AWS, Google GCP, Microsoft Azure, Oracle OCI
  Cloud Storage Interfaces: Object-Storage, Block Storage, File Storage

## Slide 16: Cloud Storage offerings
GCP
AWS
Azure
OCI

## Slide 17: Architectural Overview

## Slide 18: Cloud storage virtualization
Cloud storage virtualization is the process of abstracting and pooling physical storage resources across multiple servers or locations into a unified, logical storage system. This allows users and applications to access storage resources as though they were a single, unified entity, even though the underlying storage infrastructure may be distributed, heterogeneous, and geographically dispersed.
Key Concepts of Cloud Storage Virtualization
  Abstraction Layer
  Pooling of Resources
  Provisioning and Management
  Flexibility and Scalability

## Slide 19
Thanks !